Site Monitoring using Linux Single Board Computers
Willem A. Schreüder AC0KQ
willem@prinmath.com
HamCon Colorado 2016
This talk is available online at
http://www.prinmath.com/ham/talks/

---
Single Board Computers
- Full Linux boxes (today's topic)
  - Raspberry Pi
  - Beaglebone
- Microcontrollers (not covered)
  - Arduino
  - PICAXE
  - BASIC Stamp

---
Linux SBCs
- Runs a full Linux OS
- Usable stand alone computer or server
- Built in connectivity
  - Ethernet networking
  - USB and serial
  - General purpose IO
- Expandable using daughter boards
- Inexpensive ($50 for a working system)

---
Linux SBC Applications
- BPQ
  - Packet, WinLink & APRS
  - TNC daugter board(s)
- AllStarLink
  - Linked Repeaters using URI
- Site Monitor and Control
  - Temperature, voltage, status, relays

---
Pros and Cons
- Pros
  - Inexpensive
  - No moving parts
  - 5V power
  - Expandable
- Cons
  - SD cards corrupted by bad power

---
Raspberry Pi
- Most Popular
- Best supported
- rPi2 most powerful
- Lots of USB ports
- Lots of daughterboards
- No analog inputs
- $35 plus SD card

---
Raspberry Pi models
- Raspberry Pi
  - A/A+	700MHz CPU & 256MB SDRAM, 1xUSB
  - B 700MHz CPU & 512MB SDRAM, 2xUSB, Ethernet
  - B+ 700MHz CPU & 512MB SDRAM, 4xUSB, Ethernet
  - 2B 900 MHz Quad A7 & 1GB SDRAM, 4xUSB, Ethernet
  - 3B 1.2GHz Quad 64bit & 1GB SDRAM, 4xUSB, Ethernet
- Compute Module
  - 700MHz CPU & 512MB SDRAM
- Zero
  - 1GHz CPU & 512MB SDRAM

---
BeagleBone
- Less well supported
- Onboard eMMC
- Power & Reset buttons
- More GPIO pins
- 8 analog inputs
- $50 street price

---
Beaglebone Models
- White
  - Original 720 MHz A8
- Black
  - Most Popular 1GHz A8
- Green
  - Same CPU as Black
  - No barrel power, two Grove connectors

---
Power and Storage
- Runs on 5V DC
  - Needs clean power
- Micro SD card storage
  - Finite life
  - Bad power kills SD

---
Raspberry Pi 2B

---
Raspberry Pi Header
`

---
Pins are multiplexed
- Pins configured for different uses
- GPIO 14&15 <=> UART TxD/RxD
- GPIO 2&3 <=> I2C SDA&SCL
- GPIO 7&8&9&10&11 <=>
  SPI MOSI&MISO&SCL&CE0&CE1
- GPIO 18&19 <=> PWM 0&1
- 16-26 GPIO pins

---
Raspberry Pi Serial
- Single serial port
  - /dev/ttyAMA0
- Speeds up to 115200 bps
- TTL level signals
- By default connected to getty

---
Raspberry Pi I2C
- Inter-Integrated Circuit
  - Serial bus (a.k.a SMBus)
- Default speed 400,000 bps
- rPi has single external I2C bus
  - 127 devices
- Control lines
  - SDA (data)
  - SCL (clock)

---
Enable I2C with raspi-config 1

---
Enable I2C with raspi-config 2

---
Viewing the Bus

---
i2cdetect outputs
- Scans bus looking for devices
  - -	No Device answered
  UU	Device in use by a driver
  dd	Slave found (dd hex adress)
- Watch for devices in use from user space (e.g. BPQ)
  - can corrupt data

---
I2C devices
- TNC-Pi
- INA219 current sensor
- Temperature/pressure/RH sensors
- LCD displays
- Accelerometers
- Digitial I/O pins
- Analog<>Digital I/P pins

---
SPI bus
- Serial Peripheral Interface
- Signals (supports 2 slaves)
  - MasterOutSlaveIn
  - MasterInSlaveOut
  - Clock
  - CE0 (SS1)
  - CE1 (SS2)
- Speeds up to 250 MHz

---
raspi-config enable SPI

---
SPI Devices
- Faster than I2C, but uses more pins
- Same devices as I2C, but adds
  - GPS
  - Ethernet/WiFi/Bluetooth/RFID
  - Memory
- Full duplex

---
Beagle Bone Black

---
Beagle Bone Black

---
Pins are multiplexed
- Default configuration
  - Power&Reset Buttons
  - 4 serial ports
  - 8 analog inputs (1.8V max)
  - 1 external I2C bus (127 devices)
  - 19-128 GPIO pins
  - Switched 5V/3.3V DC

---
Restrictions
- Pins connect directly to CPU
  - Long wires are CPU antennas!
- rPi & BBB GPIO Pins are 3.3 V
  - Max current 16 mA in or out
  - Max combined output current 50 mA
- BB Analog In Pins are 1.8V

---
Device Tree
- Unix: Everything is a File
- /sys maps to hardware
  - In kernel virtual file system
- Get status by reading
- Set status by writing

---
Reading analog pins on BBB
- Enable analog pins in device tree
  echo cape-bone-iio>/sys/devices/bone_capemgr.*/slots
- Read value of pin AIN0 in mV
  cat /sys/devices/ocp.*/helper.*/AIN0
  580
- Voltage on pin AIN0 is 0.580V

---
Show pin voltages in Python 1
#!/usr/bin/python
for i in range(0,8):
   # Snarf file
   fd = open("/sys/devices/ocp.3/helper.16/AIN%d" % i)
   text = fd.read()
   fd.close()
   # Decode voltage
   V = float(text)/1000
   # Print voltage
   print "AIN%d = %5.3fV" % (i,V)

---
Show pin voltages in Python 2
./aread
AIN0 = 1.740V
AIN1 = 1.481V
AIN2 = 1.645V
AIN3 = 0.867V
AIN4 = 0.589V
AIN5 = 0.709V
AIN6 = 0.852V
AIN7 = 1.678V

---
Limitations
- Maximum voltage is 1.8V
- Use a voltage divider to increase
  - Use 1% or better resistors
  - Max 1 kohm for lower leg
- No analog in on rPi
  - use MCP3008 or similar and SPI

---
Assigning pins to GPIO
- /sys/class/gpio/export
  - Maps pin to GPIO
  - echo 18 > /sys/class/gpio/export
- /sys/class/gpio/unexport
  - Removes pin from GPIO map
  - echo 18 > /sys/class/gpio/unexport
- Root access required

---
Manipulating GPIO
- When mapped to GPIO, a new directory is created for that pin
  - /sys/class/gpio/gpioXX
- Files in this directory controls pin
  - direction = in or out
  - value = 0 or 1

---
Checking pin value
- In or out?
  - cat /sys/class/gpio/gpio18/direction
- High or low?
  - cat /sys/class/gpio/gpio18/value

---
Changing the GPIO direction
- Set pin for input
  - echo in > /sys/class/gpio/gpio18/direction
- Set pin for output
  - echo out > /sys/class/gpio/gpio18/direction

---
Changing the GPIO value
- Set pin voltage high
  - echo 1 > /sys/class/gpio/gpio18/value
- Set pin for output
  - echo 0 > /sys/class/gpio/gpio18/value

---
Setting pins at boot
- Edit /etc/rc.local
  - Runs at boot time as root
  - Enable pin 18 for output and set high
    echo 18 > /sys/class/gpio/export
    echo out > /sys/class/gpio/gpio18/direction
    echo 1 > /sys/class/gpio18/value
  - Before this runs, values are unpredictable

---
Setting many pins at boot
- Edit /etc/rc.local
  - Set ping 18, 23, 24 and 25 for output and high
    # Set GPIO ports to out
    for n in 18 23 24 25; do
    echo $n > /sys/class/gpio/export
    echo "out" > /sys/class/gpio/gpio$n/direction
    echo 1 > /sys/class/gpio/gpio$n/value
    done

---
Turn on pin 5 minutes per hour
- Edit /etc/crontab
  # This line turns on pin 18 at *:0
  0 * * * * root echo 1 > /sys/class/gpio/gpio18/value
  # This line turns off pin 18 at *:5
  5 * * * * root echo 0 > /sys/class/gpio/gpio18/value

---
python access to pins
- Import the GPIO package
  import Rpi.GPIO as GPIO
- Name the pins by their GPIO#
  GPIO.setmode(GPIO.BCM)
- Name pins by their board number
  GPIO.setmode(GPIO.BOARD)

---
python set pins for in/out
- Set pin 18 for output
  GPIO.setup(18,GPIO.OUT)
- Set pins 18,23,24&25 for output
  GPIO.setup([18,23,24,25],GPIO.OUT)
- Set ping 18 for input
  GPIO.setup(18,GPIO.IN)

---
python set/get pin value
- Set pin 18 high
  GPIO.output(18,1)
- Set pin 18 low
  GPIO.output(18,0)
- Read ping 18 value
  p18 = GPIO.input(18)

---
Input pin status
- Set ping 23 to input with pull up
- GPIO.setup(24,GPIO.IN,pull_up_down=GPIO.PUD_UP)
  - ground to activate
- Set pin 24 to input with pull down
- GPIO.setup(24,GPIO.IN,pull_up_down=GPIO.PUD_DOWN)
  - Pull up to 3.3V
- A 1k series resistor is typically a good idea

---
Important Limitations
- GPIO pins are 3.3 V
- Current limited to 16mA
- Opto-isolate
  relays

---
I2C Example: Voltage&Current
- TI INA219 I2C high side monitor
- Max 26V
- Current Sense
  40-320mV
  shunt
- Chip $2.50
- Adafruit $10

---
Adafruit Breakout
- I2C address 0x40 0x41 0x42 0x43
  - solder jumpers
- 0.1 ohm shunt
  reads to 3.2A

---
Python Usage
import Subfact_INA219 as INA219
ina = INA219()
V = ina.getBusVoltage_V()
mA = ina.getCurrent_mA()

---
Digging deeper
- Subfact_INA219 imports Adafruit_I2C
- Adafruit_I2C imports smbus
- def getBusVoltage():
  res = i2c.readU16(0x02)
  mV = (res >> 3) * 4
  return 0.001*mV

---
Reading 1wire Temperatures
- 1wire uses a single data bus
- Each device has unique address
- DS18S20 is a TO-92 temperature sensor with 0.5C resolution for $2.50
- Can use parasite
  power (but not on rPi)
  Use 4k7 pullup

---
Building the Device Tree 1
/dts-v1/;
/plugin/;
/ {
   compatible = "ti,beaglebone", "ti,beaglebone-black", "ti,beaglebone-green";
   part-number = "BB-W1";
   version = "00A0";
   exclusive-use = "P9.23";
   fragment@0
   {
      target = <&am33xx_pinmux>;
      __overlay__
      {
        bb_w1_pins: pinmux_bb_w1_pins
        {
        pinctrl-single,pins = <0x68 0x37>; /* gpio1_17,
        OMAP_PIN_INPUT_PULLUP|OMAP_MUX_MODE7 */
        };
      };
   };

---
Building the Device Tree 2
   fragment@1
   {
      target = <&ocp>;
      __overlay__
      {
        onewire@0
        {
        status = "okay";
        compatible = "w1-gpio";
        pinctrl-names = "default";
        pinctrl-0 = <&bb_w1_pins>;
        gpios = <&gpio2 17 0>;
        };
      };
   };
};

---
Building the Device Tree 3
- Edit w1.dts as shown above
- Compile with device tree compiler
  dtc -O dtb -o w1-00A0.dtbo -b 0 -@ w1.dts
  mv w1-00A0.dtbo /lib/firmware
- Enable
  echo w1 > /sys/devices/bone_capemgr.9/slots

---
Getting 1wire output
- ls /sys/bus/w1/devices
  10-000802fba50d
  10-000802fbe2f6
  10-000802fbf0f9
  w1_bus_master1
- 10 means it is a DS18S20 temp, the test is a unique serial number

---
Getting the Data
cat /sys/bus/w1/devices/w1_bus_master1/w1_master_slaves
  10-000802fbe2f6
  10-000802fbf0f9
  10-000802fba50d
cat /sys/bus/w1/devices/10-000802fbe2f6/w1_slave
  2c 00 4b 46 ff ff 0e 10 17 : crc=17 YES
  2c 00 4b 46 ff ff 0e 10 17 t=21875
Temperature of first sensor is 21.875 OC

---
Reading Temps in Python 1
# Snarf the slave list file
fd=open("/sys/bus/w1/devices/w1_bus_master1/w1_master_slaves")
text = fd.read()
fd.close()
# Split text on line breaks
slaves = filter(None,text.split("\n"))
# Sort so that order is predictable
slaves.sort()

---
Reading Temps in Python 2
# Blank dictionary
temps = {}
# Loop over devices
for slave in slaves:
      if slave=="": continue
      # Snarf device file
      fd = open("/sys/bus/w1/devices/"+slave+"/w1_slave")
      text = fd.read()
      fd.close()
      # Split lines
      lines = text.split("\n")
      words = lines[1].split(" ")
      # Get temperature
      C = float(words[9][2:])/1000
      F = 9*C/5+32
     # Add result to dictionary
      temps[slave] = "%.1fF" % F

---
Observations
- Temperature conversion occurs when you cat the file
  - About 700mS per device
- Temperature reads are best done using a separate thread
- rPi 1wire support in raspi-config

---
Show and Tell